Regulations Concerning the Sanitary Quality of Drinking Water

(Unofficial Translation)*

(As authorized by Section E1 of the Public Health Ordinance, 1940,

including all amendments up to 20 Feb., 1991)

1.Definitions (Incl. 1990 amendment)

In these regulations, the following expressions mean :-

REGION "A":-The jurisdictions of the Dimona, Eilat and Tiberias

Municipalities;of the Beit-Sh'an, Mitzpeh-Ramon and Yeroham Local

Councils; and of the Beit-Sh'an Valley, Central Arava,Eilot Region,

Jordan Valley, Ramat-Hanegev, and Tamar Regional Councils;

REGION "B":-Any area within the State of Israel not included in

REGION "A";

EXAMINATION:-An examination of drinking-water performed in a

recognized laboratory by a method fixed by the latest edition of

"Standard Methods";

MICROBIAL EXAMINATION:-An examination to reveal microbial indicators

of pollution or microbial pollutants;

COMPLETE MICROBIAL EXAMINATION:-A microbial examination to reveal

coliform, fecal coliform and fecal streptococcus bacteria; and

total plate count of bacteria;

STANDARD MICROBIAL EXAMINATION:-A microbial examination to reveal

coliform bacteria, or coliform and fecal coliform bacteria;

MICROBIAL RE-EXAMINATION:-A microbial examination to reveal coliform

and fecal coliform bacteria, of water taken from a given location -

within 24 hours of receipt of the results of a standard microbial

examination, of water taken from the same location - which

indicated that the water at that location is unfit for drinking;

CHEMICAL EXAMINATION:-An examination to discover the concentration

, or any other chemical, physical or organoleptic

property;

COMPLETE CHEMICAL EXAMINATION:-A chemical examination to discover

the concentrations of all the substances listed in Appendix A, B,

and of these regulations and, in addition, of Sodium, Potassium,

Ammonia, Nitrites, and Ultra-Violet ray absorption;

PARTIAL CHEMICAL EXAMINATION:-A chemical examination to discover the

concentrations of the following: Sodium, Potassium, Iron, Calcium,

Chlorides,Sulphates, Fluorides, Nitrates, Nitrites, Ammonia,

Alkalinity, Hardness, Total Solids, Surface-Active Agents, pH,

Color, and Turbidity;

LIMITED CHEMICAL EXAMINATION:-A chemical examination to discover the

concentration of nitrites and chlorides;

POINT OF ENTRY INTO A WATER SUPPLY SYSTEM:-Includes a point on a

water line which supplies water directly to a number of settlements

whose total population does not exceed 5000 persons;

WATER SOURCE:-As defined in Paragraph 2 of the Water Law, but which

supplies - or is intended to supply - drinking water; & including a

dual purpose(withdrawal and recharge) well;

____________

*By Y. Zohar-Assistant Chief Environmental Engineer, Department of

Environmental Health(Contact for inquiries). (Last corr. 4 Mar.,'91)

(Ref. :Regulations:-Doc. #885; Appendices:-Doc. #886)

TREATMENT FACILITY:-A facility or device which treats water

mechanically, physically, or chemically (including disinfection and

aeration) in order to improve its sanitary quality;

TREATED WATER:-Water which has undergone disinfection, or any other

process designed to improve its sanitary quality;

SANITARY SURVEY:-An investigation to discover the cause of drinking

water contamination or the cause for a possible contamination of

drinking water;

A RECOGNIZED LABORATORY:-A stationary laboratory or a field

laboratory which the Minister of Health has authorized to perform

examinations of the sanitary quality of drinking water, or any

person whom the Minister of Health has authorised to conduct a

sanitary survey in accordance with these regulations;

STANDARD METHODS:-The latest available edition of "Standard Methods

for the Examination of Water and Wastewater", APHA, a copy of

which is posted in The Public Health Library of the Ministry of

Health in Jerusalem for the perusal of all interested parties,

during hours when the library is open to the public;

THE DIRECTOR:-The Director-General of the Ministry of Health, or any

person whom he has authorized to represent him, with respect to any

or all of these regulations.

2.Water Unfit for Drinking(Incl. 1990 amendment)

Water shall be deemed unfit for drinking if any one of the

following conditions exists:-

(1)A single fecal coliform bacterium has been found, or more than

3 coliform bacteria have been found, in 100 ml. of water, in the

course of a standard microbial examination or a microbial

re-examination;

(2)(Deleted)

(3)A chemical examination has shown that a substance listed in

Appendix A, Column 1, is present in the water at a concentration

greater than that listed in Column 2;

(4)A chemical examination has shown that a characteristic or a

substance, listed in Appendix B, Column 1, is present in the

water at a concentration beyond that listed in Column 3;

(5)A chemical examination has shown that the concentration of

fluorides in the water,within the Region indicated in Appendix

C, Column 1, is greater than that listed in Column 4;

(6)A sanitary survey has been performed which indicates, in the

opinion of a Health Authority, that this water, if used as

drinking water, might harm public health.

2A.Exception(Incl.1988 amendment)

Notwithstanding Regulation 2(1), if a microbial re-examination,

which has been performed within 24 hours of the completion of a

standard microbial examination, has not indicated the presence of

a single fecal coliform bacterium, nor of more than 3 coliform

bacteria, in 100 ml. of water, the water will not be considered

unfit for use as drinking water.

3.Additional Examination(Incl.1988 amendment)

If a microbial examination has indicated the presence of between 1

and 3 coliform bacteria in 100 ml. of water, the laboratory which

performed the examination shall determine if these bacteria are

fecal coliforms.

4.Water not Meeting Maximum Desirable Limits(Incl. 1977 amendment)

If a chemical examination has shown that a characteristic or a

substance, listed in Appendix B, Column 1, is present at a

concentration beyond that listed in Column 2, then the water

supplier shall:

(1)Inform the Health Authority of this fact, without delay;

(2)Perform a sanitary survey, and/or any other activity fixed by

the Health Authority, in order to determine the cause of the

outlying concentration;

(3)Carry out the instructions of the Health Authority in order to

eliminate the cause of the outlying concentration.

4A.The Sanitary Survey(Incl.1988 amendment)

(a)A Health Authority may,with the approval of the Chief Engineer

for Environmental Health, instruct a water supplier to perform a

sanitary survey, if it finds that the results of examinations

indicate a suspicion that the water may be contaminated.

(b)A recognized laboratory, as defined in Regulation 1, shall

perform the aforesaid sanitary survey upon notification from the

Health Authority as to what is to be included in the survey.

(c)A sanitary survey performed because of microbial pollution shall

include, at the least, examinations to reveal the concentrations

of nitrates, ammonia, surface-active agents, ultra-violet ray

absorption and permanganate demand.

(d)At the completion of the sanitary survey, the laboratory shall

transmit its results to the relevant Health Authority and Local

Authority.

5.The Concentration of Fluorides in the Water(Incl.1988 amendment)

If a chemical examination shows that the concentration of fluorides

in the water in a region listed in Appendix C, Column 1 is lower

than that listed in Column 2, then the water supplier may add

fluorides to the water in order to bring them to the concentration

listed in Column 3, if the following conditions exist:

(1a)The Health Authority is satisfied that proper arrangements have

been made, in the fluoridation system design, which guarantee

that the concentration of fluorides will not exceed that listed

in Appendix C, Column 4;

(1b)The Health Authority has approved the plan of operation of the

fluoridation system, including the surveillance and testing

plans;

(2) The fluoridation system is operated in such a manner as to

ensure that the concentration of fluoride in the water does not

exceed the concentration listed in Column 4 of Appendix C;

(3) The concentration of fluoride in the water is tested daily, and

the results are recorded in a notebook (below:"the notebook");

5.(continued)

(4) The notebook shall be kept for a period of one year from the

date of the last entry recorded in it, and shall be available

at any reasonable time for the inspection of a Health

Authority, a Government Doctor, or any person authorized by the

Minister of Health.

5A.Transfer of Test Results (Incl. 1978 amendment)

(a)If one of the conditions described in Regulation 2 has been

found to exist in drinking water, the laboratory shall transfer

the results of the relevant tests without delay to the Health

Authority in whose purvey the water was sampled.

(b)Once a month, the supplier shall transfer the results, of all

the tests performed on drinking water he supplies, to the Health

Authority in whose purvey the water was sampled.

6.Water Unfit Because of Danger to Public Health (Incl. 1989 Amend.)

(a)If a Health Authority or a supplier suspects that, because of its

appearance or sanitary quality, the supply of certain drinking

water might endanger public health, that water is deemed unfit

for drinking.

(b)If, in the opinion of a Health Authority or a supplier, a

chemical test shows that certain drinking water contains toxic

substances which are not listed in Appendix A, at a

concentration which might endanger public health, that water is

deemed unfit for drinking.

(c)A supplier of drinking water - which is deemed unfit for drinking

in accordance with this regulation - must:-

(1)Cease the supply of that water immediately;

(2)Inform the Health Authority without delay;

(3)Not resume supply of that water until receiving approval for

such action by the Health Authority, and until fulfilling the

conditions set by them.

6A.Water Disinfection(1990 amendment)

Drinking water suppliers shall assure that the drinking water

which they supply shall contain, on a permanent and continuous

basis, not more than 0.5, nor less than 0.1, mg. per liter

residual chlorine, or an equivalent concentration of an equivalent

disinfectant, as approved by the director.

Exception:- If a supplier installs at least 6 disinfection

installations between 1-1-90 & 31-8-90, and submits plans and

installation dates for the installation of the full number of

disinfection installations he must install, then the

Director-General of the Ministry of Health may extend the

application of this regulation to a date not after 31-12-91.

7.Drinking Water Source(Incl. 1989 Amendment)

(a) A supplier shall not supply drinking water from a water source

(below: "a drinking water source") unless a Health Authority

has approved that source as a drinking water source.

(b) A Health Authority shall not approve a drinking water source if

one of the following exists:-

(1) The water has been deemed unfit for drinking;

(2) In a complete microbial examination, a fecal coliform

bacterium or a fecal streptococcus bacterium has been found

in 100 ml. of water, or more than 1000 bacteria have been

found in one ml. of water in a total plate count of

bacteria.

(3) The Health Authority deems the results of the chemical

examinations to be unsatisfactory.

(c) A request for approval of a drinking water source shall be

presented to a Health Authority by a supplier; the request

shall be accompanied by:-

(1) Test results of the characteristics listed in Appendices A,

B, & C of these regulations; and the results of any other

tests which the Health Authority has required;

(2) Results of a complete microbial examination.

(d) A supplier shall perform a complete microbial examination and a

limited chemical examination in a drinking water source every

three months and, in addition, before resuming water supply

from a source which did not supply water for a period exceeding

one month.

(e) A supplier shall perform a complete chemical examination of the

water of a drinking water source every 10 years, and a partial

chemical examination every 5 years. The results of the

examination shall be transferred to the Health Authority.

(f) If the concentration of any property mentioned in this

regulation is found to be greater than 80% of the maximum

permitted according to Appendices A & B of these regulations,

the supplier shall test that property at a frequency required

by the Health Authority.

8.Flushing & Disinfection of Water Systems(Incl. 1978 amendment)

Before the supply of water from a water system, whether new or

having undergone repair or revision, the supplier must:-

(1) Inform the Health Authority of the repair or revision;

(2) Flush & disinfect the system according to the instructions of

the Health Authority;

(3) Bring a sample of the water from the system to a recognized

laboratory for a microbial test, and for any other test which

the Health Authority may require.

9.Water Standing in a Reservoir (Incl. 1989 amendment)

Water which has been standing in a reservoir for a period greater

than one month may not be supplied as drinking water unless it

contains residual disinfectant, or it has been found fit for

drinking by a standard microbial examination.

10.Treated Water Examinations(Incl. 1989 amendment)

(a) Water undergoing treatment shall be examined by a microbial

examination before and after treatment at a frequency as shown

in Table No. 2 of Appendix D, or at a greater frequency which

the Health Authority may require.

(b) The disinfectant concentration in treated water shall be:-

(1) That which the director has approved;

(2) Tested at least daily.

(c) The director may require more frequent disinfectant

concentration testing, or may require installation &

operation of an instrument for continuous measurement of the

disinfectant concentration.

(d) The results of the disinfectant concentration tests shall be

reported to the examining laboratory & recorded in a notebook;

the records shall be kept for a year from the record date.

11.Examination of Water in Water Supply Systems(Incl.1989 amend.)

(a) The interval between successive sampling occasions (Column B),

and the number of samples taken on each sampling occasion

(Column C), for the microbial examination of drinking water

within a water supply system shall depend upon the population

(Column A) served by the system, as indicated in Table 1 of

Appendix D to these regulations.

(b) Upon each occasion of water sampling, as indicated in Section

11(a), the presence of disinfectant and its concentration

shall be ascertained & reported to the examining laboratory.

12.Examination of Water at Entry Points to Water Supply Systems(Incl.

1989 amendment)

The interval between successive sampling occasions (Column B),for

the microbial examination of drinking water at entry points to

water supply systems shall depend upon the population (Column A)

served by the entry point, as indicated in Table 2 of Appendix D

to these regulations.

13.Augmented Testing

If a Health Authority deems that the danger of an epidemic exists,

or that a water source is suspected of being polluted,

examinations of drinking water shall be carried out of a type and

at a frequency fixed by the Health Authority.

13A.Alternate Testing Methods

A Health Authority may issue instructions with respect to testing

methods alternate to those fixed in "Standard Methods" if it

deems that the circumstances require it on a specific occasion.

If a Health Authority so instructs, these alternate testing

methods shall be followed in place of those fixed in "Standard

Methods", as long as the occasion engendering those instructions

continues to exist.

14.Drinking Water from Dual-Purpose Recharge Wells(Incl.1978 amend.)

(a)Drinking water drawn at any time from a well - into which

drinking water is recharged at another time - (below:-a

dual-purpose well) shall be deemed suitable for use as

drinking water if the following criteria obtain:-

(1)The well has been approved as a drinking water source by a

Health Authority as stipulated in Regulation 7 (above);

(2)The water has been disinfected;

(3)A complete microbial examination, performed on a sample

taken from a point before disinfection, has shown neither

the presence of a fecal streptococcus - nor of a fecal

coliform - bacterium in 100 ml. of water;

(4)A microbial examination, performed on disinfected water,

has not shown the presence of more than 3 coliform bacteria

in 100 ml. of water;

(5)If a Health Authority has required a chemical test, the

results satisfy the requirements of these regulations.

(b)The supplier shall notify the Health Authority, in writing, of

the projected date of renewal of pumping, after which the

supplier intends to reconnect the dual-purpose well to the

water supply system.

15. Sampling (Including 1978 amendment)

(a)A person sampling drinking water for testing according to

these regulations (below:- a sampler) must be qualified to do

so, as approved by a Health Authority.

(b)The sampling of drinking water for testing by a microbial

examination shall be performed according to Section 1 of

Appendix E to these regulations.

(c)The sampling of drinking water for testing by a chemical

examination shall be performed according to Section 2 of

Appendix E.

16.The Sample until Initiation of Testing(Incl. 1978 amendment)

(a)Drinking water sampled for a microbial examination, a microbial

re-examination, or a complete microbial examination, shall be

maintained at a temperature between 4 & 10 degrees C.

(b)The tests listed in Subsection 16(a) shall be initiated not

later than six hours from the moment of sampling.

(c)A health authority, in unusual circumstances, and upon the

request of a supplier or a recognized laboratory, may waive the

six-hour requirement, provided the test is initiated within 24

hours of sampling.

17.Noting of Details with Respect to the Sample(Incl. 1989 Amend.)

(a)The sampler shall complete the form shown in Appendix 6,

including all the required details.

(b)The form and the vessel containing the sample shall bear

identical symbols.

(Ref.:Regulations-Doc.#885;Appendices-Doc.#886)

Drinking Water Quality Regulations- Appendices* P.1

Appendix A -Toxic Substances

Column 1 Column 2

Maximum Allowable Concentration

Substances (Micrograms per liter)

Mercury 1

Cadmium, Selenium 10

Arsenic, Chromium, Cyanide, Lead 50

Barium 1000

Appendix B -Substances & Characteristics of Sanitary Significance

Column 1 Column 2 Column 3 Column 4

Maximum Maximum

Substance or Desirable Allowable

Characteristic Concentration Concentration Units

---------------------------------------------------------------------

Part 1:-Substances Expressed in Micrograms per liter

Phenol 1 2 (1) Micrograms per liter

Trihalomethanes (2) (3) 100 " " "

Mineral Oil 10 300 " " "

Manganese 50 500 " " "

Iron 100 1000 " " "

Surfactants 200 1000 " " "

Copper 50 1400 " " "

---------------------------------------------------------------------

Part 2:-Substances Expressed in Milligrams per liter

Zinc 5 15 Milligrams per liter

Nitrates(as Nitrate) 45 90 " " "

Magnesium 50 150 " " "

Sulphate 250 (4) " " "

Chloride 250 600 " " "

Tot. Dissolved Sol. 800 1500 " " "

Calcium 80 (5) " " "

Hardness 200 (6) (5) " " "

---------------------------------------------------------------------

Part 3:-Characteristics Expressed in Various Units

Turbidity 1 (7) Nephelometric Units

Color 5 15 Platinum-Cobalt Un.

pH 7.0-8.5 6.5--9.5 pH Units

Taste & Odor 1 Unobjectionable Threshold Odor No.

Total Alpha Activity (3) 0.1 Becquerels per liter

Total Beta Activity (3) 1.1 " " "

---------------------------------------------------------------------

References

(1) In the presence of a characteristic objectionable odor.

(2) Chloroform,bromodichloromethane,chlorodibromomethane,& bromoform

(3) No requirement for Maximum Desirable Concentration.

(4) MAC (Max. Allowable Conc.) of SO4 (Sulphate) depends upon, and is

computed from, Mg (Magnesium) conc. in the water, as follows:

MAC of SO4(in mg./L)= 437.5 minus (1.25 times Mg conc. in mg./L)

(5) No requirement for Maximum Allowable Concentration.

(6) Hardness expressed in milligrams per liter as calcium carbonate.

(7) Up to 31.12.92:- 5 N.U. (Nephelometric Units)

From 1.1.93 to 30.06.94:- 4 N.U.

From 1.7.94 to 31.12.95:- 3 N.U.

From 1.1.96 & therafter:- 1 N.U.

Drinking Water Quality Regulations

Appendices- P.2

Appendix C

Fluoride Concentrations according to Climatic Zones

(milligrams per liter)

Column 1 Column 2 Column 3 Column 4

Minimum Maximum Maximum

Allowable Operational Allowable

Region Concentration Concentration Concentration

Region "A" 0.6 0.8 1.4

Region "B" 0.7 1.0 1.7

Appendix D

Frequency of Sampling for Microbial Testing

Table #1:-Frequency of Sampling & Number of Samples to be Taken of

Water within the Distribution System, according to Population Served

Column 1 Column 2 Column 3 Column 4

No. of Samples No. of Samples

On each Sampling Over 4-Week

Population Served Sampling Frequency Occasion Period

Up to 1,000 Once every 4 Weeks 2 2

1,001 to 5,000 " 4 4

5,001 to 10,000 " 6 6

10,001 to 20,000 " 8 8

20,001 to 30,000 Once every 2 Weeks 5 10

30,001 to 40,000 " 6 12

40,001 to 50,000 " 7 14

50,001 to 70,000 Once every Week 4 16

70,001 to 90,000 " 6 20

90,001 to 110,000 Twice per week 4 32

110,001 to 140,000 " 5 40

140,001 to 170,000 3 Times per week 4 48

170,001 to 200,000 " 5 60

200,001 to 250,000 5 Times per week 4 80

250,001 to 300,000 " 5 100

300,001 to 400,000 " 6 120

400,001 to 500,000 " 7 140

More than 500,000 " 8 160

_______________

Table #2:-Frequency of Sampling

(1)of Water at the Entrance to a Distribution System

(2)of Treated Water

Column 1 Column 2

Population Served Sampling Frequency

Up to 20,000 Once every 4 Weeks

20,001 to 50,000 Once every 2 Weeks

50,001 to 100,000 Twice per Week

More than 100,000 Daily

__________________________

Appendices-P. 3

Appendix E

Sampling

Section 1:-Sampling for Microbial Testing

1. Sample Volume - Sample volume shall be at least 100 ml.

2. Sampling Container - The sampling container shall:

a.-be clean, sterilized, and stoppered when given to the sampler.

b.-be made of transparent glass, or other transparent material which

will not affect the quality of the water sample, and which is

impervious to sterilization.

c.-be provided with a stopper which seals the mouth of the container,

and is made of material which will not affect the quality of the

water sample. After stoppering, the stopper shall be wrapped in

parchment paper or aluminum foil.

d.-contain a 2% solution of sodium thiosulphate, of a quantity equal

to 0.1 ml. for every 100 ml. of container volume.

3. Assuring that the water sample represents the water in the pipe

a.The water sample must characterize the water in the pipe rather

than the water in the tap.

b.When sampling water from a tap adjacent to a well which has not

supplied water for 24 hours or more, water shall flow from the tap

at least one-half hour (or longer, at the discretion of the

sampler) before sampling.

c.When sampling water from a tap not adjacent to a well, or when

sampling water from a tap adjacent to a well which is supplying

water - or if the well is not supplying water, but less than 24

hours have elapsed since it last supplied water - water shall flow

from the tap at least 2 minutes (or longer, at the discretion of

the sampler) before sampling.

4. Prevention of sample pollution from tap outlet

Before sampling, the outlet of the tap shall be rinsed and cleaned.

The valve shall then be shut, and the outlet disinfected by heat,

by use of a burner.

5. Sampling Procedures

a.Hold lower part of sampling container.

b.Remove stopper while touching wrapper only, without touching mouth

or neck of container.

c.In filling container, leave a two-centimeter air gap at the top,

to permit shaking in the laboratory.

d.In sampling from a stream, spring, lake or reservoir, in cases

where sampling depth is not greater than 50 centimeters, the

following additional procedures shall be followed:-

(1) Upend container.Immerse it,upside down,into water to be sampled.

(2) Turn container so that its mouth points upstream, and fill by

tilting mouth slightly upward. If there is no current, fill by

moving container gently in water.

(3) If sampling from a boat, sample from upstream side.

(4) In no case shall the sampler touch the bank or bottom of a

stream or reservoir.

e.In sampling from a point whose depth exceeds 50 centimeters, follow

directions of the Health Authority.

Drinking Water Quality Regulations

Appendices-P.4

Appendix E

(continued)

Section 2:-Sampling for Chemical Testing

1. The sample - Sampling shall be carried out according to the

instructions of the examining laboratory.

2. The sampling container

a.The container and stopper shall be of material which is easily

cleaned, and which will not affect the quality of the water

sample.

b.The container shall be clean and stoppered when given to the

sampler.

3. Preliminary steps

a.Before sampling, fill the container half-full with the water to be

sampled, stopper the container, shake vigorously, and waste the

contents of the container. Repeat this procedure three times.

b. Assuring that the water sample represents the water in the pipe

(1)The water sample must characterize the water in the pipe rather

than the water in the tap.

(2)When sampling water from a tap adjacent to a well which has not

supplied water 24 hours or more, water shall flow from the tap

at least 24 hours before sampling.

(3)When sampling water from a tap not adjacent to a well, or when

sampling water from a tap adjacent to a well which is supplying

water - or if the well is not supplying water, but less than 24

hours have elapsed since it last supplied water - water shall

flow from the tap at least 2 minutes (or longer, at the

discretion of the sampler) before sampling.

4.In sampling from a stream, spring, pond, or reservoir - proceed as

directed in Section 1, Paragraphs 5d & 5e.

------------

Appendix F

(Reg. 17 - incl. 1989 amend.)

The following details shall be noted on the sampling form:-

Person & name of organization ordering the test.

Name of sampler.

Sampling location.

Date & time of sampling.

Type of test(Routine, standard, microbial, other)

Chlorine concentration in water at time of sampling.

Signature of sampler.

---------------